The Lunascan Project - MOONWATCH - Team Report 
May 11, 2012

| TARGETS: | Western Half | No Specific Targets This Scan |
| --- | --- | --- |

BOS 3:52:35 Quad, calibrated with Atomic Clock, but this framegrab was taken at 4:01:08 Q MISSION PLAN: DOB Driver II scans of terminator and to the W, targeting any objects in Western Hemisphere. Primary craters washed out as this was 1-2 days earler than optimum, but still possible imaging of anomalies or fastwalkers.. Camera 1 mini finder switchable to CCD camera Camera 2 Internal Camera 3 LPI/VMA graphics. (LPI not used) Camera 4: SSI/CCD/ C-8. . . CAMERAS: CAMERA ONE POSITION ON QUAD * Finder: mini cam CAMERA TWO POSITION * Internal camera CAMERA THREE POSITION Compaq Presario sr1218nx computer (1) Digital to Analog Converter 1; TEP-100 Elite Pro II Aperture video recorder VHS2 VIRTUAL MOON ATLAS graphics CAMERA FOUR POSITION Dell computer Digital to Analog Converter 2: TEP-100 Elite Pro II Aperture video recorder DVR2 No graphics used All camera outputs to Quad / VHS1 / Q Select DVR1 SSI Camera CCD, (Celestron Neximage Solar System Imager / Charge Coupled Device) OPTICS, prime focus. 5 mm VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 LPI Camera Not used CMOS, (Meade Lunar Planetary Imager / complementary metal oxide semiconductor) OPTICS, prime focus. 6 mm. VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 Celestron C-8 SCT 8” optical tube 2032 mm f/l F10 Resolution at lunar range = 0.68 / .81086 mi or 4281.36469 feet (30.19' X 60 = 1811.4" /.68' resol = factor of 2663.82353 2160 miles / 2663.82353 = .81086 mi resolution) 0.621 mi/km 1 m = 3.28 ‘ CONFIG No diagonal or binoc viewer. Extended hand control DOB Driver II REPORT NOTES 2032 mm / 5 mm = 400x . Lunar range 375,000 km = 233,000 mi / 400 = 600 mi sim range LOS WWV audio. No recordings. BOS 3:52:35 Quad Time fix from DVR1 at 1:11:00 elapsed with DVR2 at 1:11:49 counters. DVR2 has 49 sec lead Video on with target acquisition at 3m 57sec SNS (Screen Not Set). Set at 20m35s elapsed Quad S rec graphics off at 4:10:26 and VMA on for duration Finder cable problem. [Remove transm from MB to Lab, place on SPU for wireless] No tape in VCR1, neg Quad recordings Bad picture on Qselect Mon. Reason unknown Desktop on Mon 4 keeps shutting down but set at 120mins DVR1 Stop DVR2 AOS at 5m32s Window not set No baffle Multiple dust mites in high light areas Terminator shots good No sound, good images, unredacted Recordings on but no sound VHS1 WWV Quad audio not recd and no tape in drive VHS2 Used for VMA but not saved / CMOS cam not used DVR1 no audio DVR2 no audio VGA computer display from Celestron CCD camera, very good. Recording from DVR analyzed No anomalies FW at 31m31s elapsed / Bird Ray on Copernicus peak needs framegrab Cam 1 quadrant needs overlay for targeting. Problem with reception of WWV signal from Fort Collins still an issue. Scope Note needs to be added to op manual to - Balance on scope needs to be reviewed - F discs need to be in place before BOS - Finders (both) and scope need to be aligned before BOS. - Orientation of Moon needs to be performed before BOS. - Due to high angle of most shots and the new mount the binoc viewer and diagonal must be used. - Post mode sheet for DOB Driver II in cab / learn modes - Calibrate DOB Driver II for BLASH 1. Compaq Presario sr1218nx XP home, dvd rom, cd burner, 2.67 GHZ processor, 760 mb RAM, 80 GB hard drive T