The Lunascan Project - MOONWATCH - Team Report 
June 10, 2012

| TARGETS: Multiple | Eastern Limb | Routine Targets |
| --- | --- | --- |

BOS 4:09 am local MISSION PLAN: Routine scans with 62.0 illumination Lunar range at 386,967 km / 246,306 miles / lunation 20.27 days / colongitude 159.1 Simrange 600 miles Quad batt fail date/time error Says 06/09/2012 11:53:48 Time fix for Q at 8h30m CUT = 0:01:04 elapsed Target Acq at 1m43s elapsed EOS at 47:20s elapsed Q time correction at 11m56s elapsed = 20120610 4:09:54 Quad Findercam malfunction Good imaging with good WWV Camera 1 mini finder Camera 2 Cargo cams (1 &2) Camera 3 LPI/VMA graphics. (LPI not used) Camera 4: SSI/CCD/ C-8. . . CAMERAS: CAMERA ONE POSITION ON QUAD * Finder: mini cam CAMERA TWO POSITION * Cargo cameras color minicam & night vision CAMERA THREE POSITION Compaq Presario sr1218nx computer (1) Digital to Analog Converter 1; TEP-100 Elite Pro II VIRTUAL MOON ATLAS graphics CAMERA FOUR POSITION Dell computer Digital to Analog Converter 2: TEP-100 Elite Pro II Aperture video recorder DVR2 No graphics used All camera outputs to Quad / VHS1 / Q Select DVR1 SSI Camera CCD, (Celestron Neximage Solar System Imager / Charge Coupled Device) OPTICS, prime focus. 5 mm VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 LPI Camera Not used CMOS, (Meade Lunar Planetary Imager / complementary metal oxide semiconductor) OPTICS, prime focus. 6 mm. VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 Celestron C-8 SCT 8” optical tube 2032 mm f/l F10 Resolution at lunar range = 0.68 / .81086 mi or 4281.36469 feet (30.19' X 60 = 1811.4" /.68' resol = factor of 2663.82353 2160 miles / 2663.82353 = .81086 mi resolution) 0.621 mi/km 1 m = 3.28 ‘ CONFIG No diagonal or binoc viewer. Extended hand control DOB Driver II REPORT NOTES QUAD VHS Data BOS 4:09:54 corrected from Q batt fail error of 06/09/2012 11:53:48 Time fix at 8h30m CUT = 0:01:04 elapsed Target Acq at 1m43s elapsed Malfunction of Findercam to Quad Good A/V with WWVR near Moonbuggy, no ant Quad datatape shows EOS at 47m20s elapsed DVR1 Data Good images WWV soundtrack malfunction (not sure what session this problem began on) DVR2 No images at BOS Time fix at 8h30m CUT Target Acq and focus at 2m13s elapsed Sharp limb LOA at 9m56s elapsed (while correcting Quad time/date error) Regain Acq at 15m51s elapsed Start of second TA 22m48s Additional time fix at 9h4m CUT = 35m31s elapsed 38m point shows degradation of signal to to weather EOS at 47:20s elapsed No anomalies observed. Cargo Cam VHS3/DVD Good images and WWV feed Best images with blue cockpit lights 1. Compaq Presario sr1218nx XP home, dvd rom, cd burner, 2.67 GHZ processor, 760 mb RAM, 80 GB hard drive T