The Lunascan Project - MOONWATCH - Team Report 
November 1, 2011

| TARGETS: | SECTIONS: | SINUS |
| --- | --- | --- |

The target is MISSION PLAN: Routine scans of terminator, targeting section Camera 1 mini finder switchable to CCD camera Camera 2 Internal Camera 3 LPI/CMOS/ VMA graphics. Camera 4: SSI/CCD/ C-8. . . CAMERAS: CAMERA ONE POSITION ON QUAD * Finder: mini cam CAMERA TWO POSITION * Internal camera CAMERA THREE POSITION Compaq Presario sr1218nx computer (1) Digital to Analog Converter 1; TEP-100 Elite Pro II Aperture video recorder VHS2 VIRTUAL MOON ATLAS graphics CAMERA FOUR POSITION Dell computer Digital to Analog Converter 2: TEP-100 Elite Pro II Aperture video recorder DVR2 No graphics used All camera outputs to Quad / VHS1 / Q Select DVR1 SSI Camera CCD, (Celestron Neximage Solar System Imager / Charge Coupled Device) OPTICS, prime focus. 5 mm VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 Wratten filter, #11 yellow LPI Camera Not used CMOS, (Meade Lunar Planetary Imager / complementary metal oxide semiconductor) OPTICS, prime focus. 6 mm. VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 Celestron C-8 SCT 8” optical tube 2032 mm f/l F10 Resolution at lunar range = 0.68 / 0.621 mi/km 1 m = 3.28 ‘ CONFIG No diagonal, extended hand control DOB Driver II REPORT NOTES DVR1 15:36:18 Quad time BOS No sound 15:42:17 Cam 3 is VMA 15:43:06 Garb Quad image 15:43:32 is 07 M 25 s elapsed 20 10 09 cam 4 full screen 20 18 51 stop temp 19 24 45 time correction 0 27 09 E 19 31 27 grab cap 025 check later 20 10 10 01 12 56 E full screen finally 20 16 41 01 19 27 E tycho grab 026 20 29 00 stop 2032 mm / 5 mm = 400x . Lunar range 396,200 km = 242,935 mi / 400 = 600 mi sim range Target Theophilus 2.0” on CRT @ 15.0” = FOV= 450 mi No audio on recordings by DVR 1 or 2 DVR1 DVR2 No sound, better images, unredacted Grabbed scans from same periods Cap 020 021 Recordings on but no sound VHS1 Quad audio on but no sound VHS2 Used for VMA but not saved / CMOS cam not used DVR1 no audio DVR2 no audio Command Center Scope Finder worked better anchored to mount rather than scope, but needs to be screwed down instead of velcroed. Note needs to be added to op manual to - F discs need to be in place before BOS - Finders (both) and scope need to be aligned before BOS. - Orientation of Moon needs to be performed before BOS. - Due to high angle of most shots and the new mount the binoc viewer and diagonal must be used. - Post mode sheet for DOB Driver II in cab / learn modes - Calibrate DOB Driver II for BLASH 1. Compaq Presario sr1218nx XP home, dvd rom, cd burner, 2.67 GHZ processor, 760 mb RAM, 80 GB hard drive T