The Lunascan Project - MOONWATCH - Team Report 
July 25, 2012

| TARGETS: | Eastern Hemisphere | Multiple Targets |
| --- | --- | --- |

BOS CREW COMPLIMENT: Fran Ridge MISSION PLAN: Wednesday 25 July 2012 Central Daylight Time SUN Begin civil twilight 5:18 a.m. NA Sunrise 5:48 a.m. NA MOON Moonset 11:01 p.m. on preceding day Moonrise 12:43 p.m. Date: 2012-07-25 21:00:00 (9 PM) Distance: 367925Km Apparent diameter: 32.48' Colongitude: 358.7 Phase: 94.3 Lunation: 6.86 days Illumination: 46.3% Simrange 600 miles Camera 1 mini finder Camera 2 Cargo cams Camera 3 VMA graphics/T1392 E-M Datalogger/LPI (LPI not used) Camera 4: SSI/CCD/ C-8. . . CAMERAS: CAMERA ONE POSITION ON QUAD * Finder: mini cam CAMERA TWO POSITION * CabCam color minicam/w illum blue instr lights * CabCam camera w/night vision hardlined to lab CAMERA THREE POSITION Compaq Presario sr1218nx computer (1) Digital to Analog Converter 1; TEP-100 Elite Pro II VIRTUAL MOON ATLAS graphics left EM DATALOGGER T1392 right set for ( X ) MilliGauss ( ) MicroTesla ( ) KII on rod for CabCam pickup CAMERA FOUR POSITION Dell computer Digital to Analog Converter 2: TEP-100 Elite Pro II Aperture video recorder DVR2 No graphics used All camera outputs to Quad / VHS1 / Q Select DVR1 SSI Camera CCD, (Celestron Neximage Solar System Imager / Charge Coupled Device) OPTICS, prime focus. 5 mm VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 LPI Camera Not used CMOS, (Meade Lunar Planetary Imager / complementary metal oxide semiconductor) OPTICS, prime focus. 6 mm. VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 Celestron C-8 SCT 8” optical tube 2032 mm f/l F10 Resolution at lunar range = 0.68 / .81086 mi or 4281.36469 feet (30.19' X 60 = 1811.4" /.68' resol = factor of 2663.82353 2160 miles / 2663.82353 = .81086 mi resolution) 0.621 mi/km 1 m = 3.28 ‘ CONFIG ( ) Diagonal and ( ) binoc viewer. Extended hand control DOB Driver II REPORT NOTES QUAD DataDisc from VHS1 START at 21:08:19 Q CabCam is ON Cam 2 Pos VMA/EM Datalogger is ON Cam 3 pos DL set at mTesla Neg WWV or SW carrier WT is working, time fix verifies Q time FinderCam is ON & target onscreen at 21:09:16 Q SSI (Cam4) is ON & focused at 2m46s elapsed = 21:11:04 Q Cap 009 is Quad data full WT Time Fix at 1h30m51s el = 22:39:15 CUT Cam 4 OFF EOS DVR2 Very good imaging with limb slightly less than sharp WWV signal very good but intermittant. Tuneable receiver near van on batts. DW position EMF datalogger injection with VMA graphics set on microTesla first hour then switched to milliGauss. Meade Barlow inserted in telescope back then SSI cam. Doubled image with some blur due to sky conditions. Good A/V on VCR1,3, DVR2 Quad Select DVR2 3m21s elapsed target acquisition Good volume on audio but no WWV carrier Sharp limb Capture 001 rays 12m19s el Good WWV at 17m09s el Time fix at 2h38m CUT 29m54s el Barlow 30m37s el Normal 36m00s el WT inaudible LOT & stop Time fix 3h5m CUT was 56m53s el Cap 005 = ray connections 3h27m CUT = 1h18m53s el LOT Reestablished 1h22m25s el Barlow 2X Back to normal 1h24m57s el 1h31m13s el LOT Cargo Good video. Bad sound connection/little or no audio. Analysis of DVR1 as follows: SUGGESTIONS 1. Compaq Presario sr1218nx XP home, dvd rom, cd burner, 2.67 GHZ processor, 760 mb RAM, 80 GB hard drive T